RequireJS
# Definitions
A:
B:
C:
# Defining a module
each of the following are in their own js file
## Simple object literal module (note: values can be functions)
define({
key1: “value1”,
key2: “value 2”
});
Accessible via the path to the js file (from the baseUrl) --- as with all modules
## Object literal module with setup (definition function)
define(function(){
// setup code here
return {
key1: “value1”,
key2: “value 2”
};
});
## Definition function with dependency
define([“./cart”, “./inventory”], function(cart, inventory){
return {
key1: “value1”,
addToCart: function(){
inventory.decrement(this);
cart.add(this);
},
color: “blue”
};
}
cart.js and inventory.js must be in the same directory as the module for ./cart and ./inventory paths to work
## Function module (with dependencies)
define(['./my/cart', 'my/inventory'],
function(cart, inventory){
return function(title) {
return title ? (window.title = title) : inventory.storeName + ' ' + cart.name
}
}
## Named function module [DON'T DO THIS. Makes modules less portable]
define('modules/title',
['my/cart', 'my/inventory'],
return function(cart, inventory){
//code and stuff
}
);
# Running modules
Create a file with a name like “main” etc. accessible from index.html
## <script data-main="path/to/start/module" src="scripts/require.js"></script>
- path/to/start/module :: start module is the entry point for a requirejs app, which runs the modules based on specified dependencies etc
- scripts/require.js	:: path to requireJS library itself
- Should be placed either at the end of the <body> section, or end of the <head> section.
## require.config(optionsObj) [[[in entry point]]]
Called in a script accessed using the data-main entry point in index.html - :
<script data-main="scripts/main" src="scripts/require.js"></script>
path scripts/main.js should then contain the require.config object
## require(['moduleDep1'], function(dep1){ /* code here runs after deps load*/ });
That's it.Usually preceded by a config file.
## Full example for running modules (in entry point)
requirejs.config({
    baseUrl: 'scripts',
    paths: {
        jquery: [
        'https://ajax.googleapis.com/ajax/libs/jquery/1.11.3/jquery.min'
        ],
        bootstrap: '../public/bootstrap/js/bootstrap.min',
        lodash: '../public/lodash/lodash'
    }
});

requirejs(['main', 'testaddedjsfile', 'lodash', 'jquery'], function(main, ta, _){
// code that uses jQuery, lodash, or either the main or testaddedjsfile module

requirejs(['bootstrap'], function(bootstrap){
//code that uses bootstrap library. Ensures bootstrap loads AFTER jQuery.
});

});
# Configuration– require.config optionsObj properties
All of these are within optionsObj in the following:
## optionsObj.baseUrl
Path all other paths are relative to, in paths (and in called modules) – see below...
## optionsObj.paths
Object literal containing keys corresponding to module names, and values corresponding to module locations
require.config({
baseUrl: 'scripts',
paths: {
'compute': 'compute/main',
'jquery': '../libs/jquery'
}
});
Henceforth, when require(['compute']) is called, scripts/compute/main.js will be called (the module is now called 'compute')
## optionsObj.waitSeconds
number of seconds to wait before giving up on loading a script. Default is 7.
require.config({
....
waitSeconds: 15
...
});	// This will wait 15 seconds before giving up on loading scripts
## optionsObj.shim
## optionsObj.bundles
## optionsObj.map
## optionsObj.config [HOW TO PASS DEPENDECIES INTO MODULES]
Lets you pass config info into a module (or modules)

requirejs.config({
    config: {
        'bar': {
        size: 'large'
        },
        'baz': {
        color: 'blue'
        }
    }
});

// ... IN ANOTHER FILE (bar.js) ...

define(function (require, exports, module) {
    var size = module.config().size;	//Will be the value 'large'
});

// ... IN ANOTHER FILE (baz.js) ...

//baz.js which uses a dependency array. it asks for the special module ID, 'module':
//Differences-between-the-simplified-CommonJS-wrapper-and-standard-AMD-define#wiki-magic
define(['module'], function (module) {
    var color = module.config().color;	//Will be the value 'blue'
});
## optionsObj.packages
## optionsObj.nodeIdCompat
## optionsObj.context

## optionsObj.deps
## optionsObj.callback
Function to execute after deps have been loaded.
# Other
## Generate URLs relative to module
To do this, ask for require as a dependency, then run require.toUrl() to generate the URL e.g.
define(["require"], function(require) {
    var cssUrl = require.toUrl("./style.css");
});
## Circular dependencies

## Undefining a module

A
--> (a)